## Slide 1: Leveraging LLMs for Adaptive and Secure UAV Control
PhD Dissertation Proposal
Balakrishnan Dharmalingam
Oakland University, 2025
DAC Members:
Dr. Anyi Liu
Dr. Subra Ganesan
Dr. Xiaodong Deng
Dr. Mohammad Wardat

## Slide 2: Outline
Introduction and background
Research Problems
Research Objectives
Approach
Methodology
Contribution
Timeline
Q&A

## Slide 3: Acknowledgements
Would like to thank Dr. Anyi Liu and Dr. Subra Ganesan for their valuable guidance and advice
Would like to thank Dr. Deng and Dr. Wardat for their comments and feedback
Would like to recognize OU Students Ibrahim, Sid, Brett, and Raj for their contribution to collect sensor data, fine tuning LLMs

## Slide 4: Introduction and Background
UAV – Definition
Applications
Control Mechanisms
  PID, MPC
Challenges

## Slide 5: UAV
Unmanned Aerial Vehicles
  Drones, VTOL, Fixed Wing planes
  Autonomous
Components
  UAV, GCS, Radio Telemetry, Onboard computer, power bank
  Onboard Sensors such as GPS, LiDAR, Cameras, Inertial Measurement Unit (IMU)
Applications
  Military
    Surveillance
    Precision strikes
    Reconnaissance
  Disaster management
  Navigating hazardous environment
  Agricultural Monitoring
  Consumer applications
    Package Delivery
    Aerial Photography

## Slide 6: UAV Flight Management Systems
Firmware
  ArduPilot
  PixHawk (PX4)
    NuttX OS – Linux like OS
    System architecture in Appendix

## Slide 7: Control Mechanisms
Proportional Integral Differential (PID) Controllers
  Changes the outputs of actuators based on sensor feedback
  Details in Appendix
Model Prediction Control (MPC)
  Optimize control within a prediction horizon
Effective in structured contexts but less effective in
  Adverse weather
  Evolving mission requirements
Lack adaptability in dynamic/unpredictable settings
Require extensive data, calibration, domain knowledge
Not scalable
May not work on all UAV platforms or mission profiles

## Slide 8: Challenges
Adaptive Control
  Dynamic Environment - Weather, Obstacles, etc.
  Maintains flight and mission performance stable
Cyber Security
  Flight Management Systems lack Cyber Security
  Adversaries inject malicious data thru GCS, Wi-Fi, GPS Spoofing

## Slide 9: Large Language Models
Large – Data and hyper parameters (Weights and Bias)
Natural Language processing (NLP)
  In-context learning
  Contextual reasoning
  Infers patterns from data
  Adapts to new tasks with minimal additional training
  Can be finetuned for different problem domain
E.g., Llama 4, DeepSeek, GPT-5, Grok 4, Anthropic Sonnet

## Slide 10: State of the Art

## Slide 11: Literature Review
Control Vs. Security
Control engineers focus on stability and gain margins; security researchers focus on threat models. The interaction between controllers and security measures is rarely analyzed.
LLM Practicality
Data Gaps
Most LLM applications for robotics are proofs of concept. Questions about latency, energy use, and resilience under attack remain wide open for real-time drone deployment.
There is a lack of datasets combining flight telemetry, network traces, and annotated attacks, making it difficult to gauge robustness against adversaries.

## Slide 12: Research Gap
Not many research done on using LLMs to control UAVs
Not many research on distributed architecture to overcome limited computing resources in UAVs

## Slide 13: UAV Control using LLMs
LLMs can:
  Integrate diverse data streams (sensors, commands, regulations)
  Detect cyber anomalies using historical data
  Optimize flight trajectories in response to real-time updates
  Dynamically revise decision rules and self-adjust

## Slide 14: Research Problems
Investigate integrating LLMs into UAV control systems to enhance adaptability, autonomy, and cybersecurity.
Integration of LLMs into UAV systems is challenging
Focus: Can LLMs enhance adaptability, autonomy, cybersecurity in UAVs?

## Slide 15: Research Objectives
Obj 1: Collect dataset using simulations (HITL/SITL), hacking, fuzzing.
Obj 2: Utilize LLM for MITM attacks, generate fake data for training.
Obj 3: Finetune LLMs using PEFT, RLHF, SFT for anomaly detection, path optimization, threats.
Obj 4: Use LLMs for anomaly detection, forecasting; select task-specific models.
Obj 5: Evaluate framework vs. traditional controls (precision, recall, F1, accuracy, latency, resilience).

## Slide 16: Publications
B. Dharmalingam, A. Liu, S. Ganesan, and S. Roy. FineObfuscator: Defeating reverse engineering attacks with context-sensitive and cost-efficient obfuscation for android apps. In 2022 IEEE International Conference on Electro Information Technology(eIT), pages 368–374, 2022. doi: 10.1109/eIT53891.2022.9837111.
B. Piggott, S. Patil, G. Feng, I. Odat, R. Mukherjee, B. Dharmalingam, and A. Liu. Net-gpt: A llm-empowered man-in-the-middle chatbot for nmanned aerial vehicle. In 2023 IEEE/ACM Symposium on Edge Computing (SEC), pages 287–293, 2023. doi: 10.1145/3583740.3626809
B. Dharmalingam, I. Odat, R. Mukherjee, B. Piggott and A. Liu, "Heterogeneous Generative Dataset for UASes," 2023 IEEE International Conference on Mobility, Operations, Services and Technologies (MOST), Detroit, MI, USA, 2023, pp. 229-230, doi: 10.1109/MOST57249.2023.00034.
B. Dharmalingam, B. Piggott, G. Feng, R. Mukherjee, and A. Liu. Aero-llm: A distributed framework for secure uav communication and intelligent decision-making. In Proceedings of the ICCCN 2024 Conference. IEEE, 2024.

## Slide 17: Contributions
Construct HGDAVE dataset for UASes (CAVs/UAVs).
Design LLM-powered MITM chatbot (Net-GPT).
Optimize task-specific LLMs using SFT/RLHF.
Develop distributed LLM architecture for UAV missions.
Implement anomaly detection using LLM.
Evaluate framework in real/simulated scenarios.
Benchmark Aero-LLM vs. standard controllers.

## Slide 18: Approach
Collect comprehensive data from sensors
Pre-process the data - Missing data, normalizing data, extrapolating, remove noise, etc.
Select LLM models for Time series data
Finetune foundational model with UAV sensor data collected
  Use Ubuntu with GPU
  Use cloud containers with GPU
Use the finetuned model for controlling UAV and anomaly detection

## Slide 19: Methodology – Data Collection
GCS, Simulation, Physical hacking, Fuzzing, TCP, UDP, MavLink
Pre-process sensor/TCP/UDP data
Select foundation models for tuning
  Header fields selected for fine tuning

## Slide 20: Methodology - Simulation
PX4 Autopilot Firmware
Simulation Types: SITL (software-only), HITL (hardware-integrated).
Simulators:
  Gazebo
  jMavSim

## Slide 21: Methodology - SITL
SITL Setup: Run on computer, simulators like Gazebo.

## Slide 22: Methodology - HITL
HITL Setup: Real hardware + simulator for validation.

## Slide 23: Methodology – Manual Hacking

## Slide 24: Methodology - Fuzzing
PGFuzz
  Manipulates input data from three different sets:
    Commands
    Parameters
    Environmental factors

## Slide 25: LLM - Finetuning
Sensor data is Time Series data
LLM for Time Series
  Timesnet
  Time-LLM
    Based on Llama-2-7B
QLoRA
RLHF

## Slide 26: System Architecture

## Slide 27: System Design
Data Collector
  Integration: LLM generates commands via offboard control (MAVLink messages).
  Data: µORB topics (position, attitude, sensors), MAVLink traffic.
  Generation: Adverse weather, obstacles, missions for training.

## Slide 28: System Design
Fine tuner
  Preprocessor: Preprocess collected data
  Fine tune: Train foundation models using preprocessed data
  Deploy fine tuned models
    Onboard
    Edge
    Cloud

## Slide 29: System Design
Online Controller
  Monitor sensor data
  Infer if anomalous
  Mitigate attack

## Slide 30: System Design
Offline Processor
  Evaluate performance
  Adjust parameters if needed

## Slide 31: Threat Model
Attacks: Network (jamming/spoofing/MITM), sensor manipulation, software vulns, insider threats.
Infrastructure: Reliable network, GPUs at edge/cloud.
Launched Attacks: MAC spoofing, session hijacking, etc. (C, P, I, A impacted).

## Slide 32: Threat Model
Network Attacks
Unauthorized access, data breaches, and disruption of communication channels.
Sensor Manipulation Attacks
Adversaries may attempt to tamper with or spoof sensor data, leading to incorrect decisions and catastrophic consequences.
Software vulnerabilities
Software/firmware vulnerabilities may lead to the compromise of confidentiality, integrity, availability and authenticity of the UAV system.
Insider threats
Malicious insiders with access to the UAV system potentially sabotage operations or leak sensitive information.

## Slide 33: Fine Tuning
Process: Train foundation model with domain data for prompt-based inference.
Data: TCP/UDP (headers: ports, seq, ack), MavLink sensors (time-series from Ulog to CSV).
Models: TimesNet (anomaly), Time-LLM (forecasting).
Techniques: SFT, RLHF, QLORA (params in table 3.4).

## Slide 34: Fine Tuning
Research Paper:
B. Dharmalingam, B. Piggott, G. Feng, R. Mukherjee, and A. Liu. Aero-LLM: A distributed framework for secure UAV communication and intelligent decision-making. In Proceedings of the ICCCN 2024 Conference. IEEE, 2024
2 Models for different tasks:
  TimesNet – Anomaly Detection
  TimesLLM – Forecasting

## Slide 35: Fine Tuning - TimesNet
TimesNet Tuning
  Collect UAV sensor data, such as altitude and GPS coordinates
  Preprocess data that includes imputation of missing values and feature scaling
  Divide the dataset into subsets, ensuring a mix of normal and anomalous points, and label them
  Initialize with pre-trained weights, then set the fine-tuning parameters, such as sequence length and learning rate
  Training on the dataset until performance plateaus
  The refined model is saved and ready for real-time anomaly detection in UAV operations

## Slide 36: Fine Tuning – Time-LLM
Time-LLM Tuning
  Collect UAV sensor data, such as IMU
  Preprocess data filling in missing values, normalization
  Divide the dataset into training, validation, and test subsets
  Initialize with pre-trained weights, then set the fine-tuning parameters, such as sequence length and learning rate
  Tokenize data to match Time-LLM's language
  Train on the dataset until performance plateaus
  Evaluate on the test set to gauge its forecasting performance such as accuracy and precision by calculating MAE and MSE
  The optimized model is saved for future predictions

## Slide 37: Parameters for Fine Tuning

## Slide 38: Metrics
Variance of Anomalous Data
Resilience of TimesNet Model
  Can handle variations in the data without significant degradation in performance
Performance Metrics Stability
  Metrics remain largely unaffected despite the variance
Effective Anomaly Detection
  Consistently identifies anomalies effectively

## Slide 39: Metrics
Impact of Batch Size
Batch Size of 48 and Above
  Batch sizes of 48 and higher significantly reduce the elapsed processing time
  Increasing the batch size beyond 48 does not proportionally reduce the elapsed time
Optimization Insights
  Larger batch sizes no longer contribute to significant time savings.
  Batch size of 48 is optimal for balancing performance and processing efficiency.

## Slide 40: Metrics

## Slide 41: Framework Design
Distributed: Onboard (lightweight for anomaly/decisions), Edge (fusion/analysis), Cloud (analysis/simulations).
Subsystems: Data Collector, Fine-Tuner (pre-processing), Online Controller, Offline Processor.
Workflow: Collect → Preprocess → Tune → Deploy → Evaluate → Harden.

## Slide 42: Approach
Models: TimesNet (sentinel), Time-LLM (forecaster), LLM Toolformer (policy).
Foundations: SFT, RLHF, ZeRO/PEFT for efficiency.
Data Pipeline: Acquisition, Preprocessing, Feature Eng.
Distributed: Onboard (low latency), Edge (higher capacity), Cloud (batch).
Assumptions: PX4 stack, intermittent links, heterogeneous compute, adversaries.

## Slide 43: Current & Expected Outcomes
HGDAVE Dataset: For UASes, from scripts, fuzzing, exploits; use Digital Twin.
Robust, relevant for LLM training.

## Slide 44: Outcomes - Malicious UAV Model (Net-GPT)
Analyzes/executes MITM; synthetic packets via LLMs.
Evaluation: Llama-2-13B/7B ~95% accuracy; smaller models ~75%.
Cost-Efficiency: Analyzed for configs (fig 4.1).

## Slide 45: Timeline – Roadmap
Apr 2023
Dec 2023
Apr 2024
Dec 2024
Nov 2025
HGDAVE
Collect Network and Mavlink Sensor Data and publish paper
FineTune LLM
Fine tune timeseries based LLM foundation models and publish paper
NetGPT
Design Net-GPT using LLM and publish paper
Aero-LLM
Design Aero-LLM distributed framework and publish paper
Dissertion Propoal
Proposal Defense Presentation
Dec 2025
Dissertation Defense
Defend Dissertation
Notes: © Copyright PresentationGO.com – The free PowerPoint and Google Slides template library

## Slide 46: Q&A
- Thank you for your attention.
- Questions?

## Slide 47: References
Haixu Wu, undefined., et al, "TimesNet: Temporal 2D-Variation Modeling for General Time Series Analysis," in International Conference on Learning Representations, 2023.
Jin, M., et al, "Time-LLM: Time series forecasting by reprogramming large language models," in International Conference on Learning Representations (ICLR), 2024.
X. Liu, undefined. H. Ning, undefined. Y. Xu. "A Survey on Industrial Internet of Things: A Cyber-Physical Systems Perspective," in IEEE Internet of Things Journal, vol. 6, no. 5, pp. 855-869, 2024.
S. Gupta, undefined. P. Kumar. "Enhancing CPS Architectures with SOA for Industry 4.0 Enterprise Applications," in IEEE Transactions on Industrial Informatics, vol. 10, no. 3, pp. 567-580, 2024.
R. Patel, undefined. M. Gupta. "AI and IoT in Industry 4.0: Trends and Applications," in Springer AI and Industry Journal, vol. 15, no. 4, pp. 210-230, 2024.
M. Zhang, undefined. Q. Wei. "A Systematic Review of Data Quality in CPS and IoT for Industry 4.0," in International Journal of Data Quality, vol. 8, no. 2, pp. 123-145, 2024.
Shumaila Javaid, undefined. Nasir Saeed, undefined. Bin He, "Large Language Models for UAVs: Current State and Pathways to the Future," 2024.

## Slide 48: PX4 Autopilot
System Architecture

## Slide 49: Multicopter Control Architecture

## Slide 50: FC and Companion Computer

## Slide 51: Fine Tuning - Implementation
Ubuntu 22.04
Python 3.12
PyTorch
Nvidia RTX 4090 GPU

## Slide 52: Code Repo
FineTuning code in GitHub
  https://github.com/dbalki/px4.git
  https://github.com/dbalki/handshakeGPT.git